## Slide 1
WATER AND POWER DEVELOPMENT AUTHORITY
2nd INTERANTIONAL HYDROPOWER CONFERENCE
DECEMBER 2022
DIAMER BASHA DAM PROJECT

## Slide 2: WHY HYDROPOWER
Economic Resource of Energy
Renewable and Clean Resource
Eco Friendly
Flood Mitigation

## Slide 3
PAKISTAN WATER RESOURCES
Annual Surface Water Availability
145 MAF
Storage Capacity
Ground Water
13.5 MAF
55 MAF
26 MAF
Water Available for additional Storage

## Slide 4
Chart: 
| WAPDA | HYDEL IPPS | GENCOS | THERMAL IPPS | INDUSTRIAL PLANTS | NUCLEAR | WIND | SOLAR | BIOFUELS
ENERGY MIX (BILLION UNITS) | 28.7 | 1.82 | 6.8 | 68.71 | 0.22 | 10.87 | 2.9 | 0.71 | 0.71
Total Generation 121 Billion Units/Year
WAPDA’s Contribution 37 Billion Units/Year (28.7%)
THE ENERGY DYNAMICS OF PAKISTAN

## Slide 5
ENERGY MIX
IDEAL HYDEL THERMAL MIX
70:30
PRESENT HYDEL THERMAL MIX
30:70

## Slide 6
5
PAKISTAN’S HYDROPOWER POTENTIAL
Total Potential= 100,000 MW
Identified Potential= 62,796 MW
Tapped= 9,400 MW
Chart: 
| Indus Corridor | Jhelum Corridor | Chitral, Swat & Kabul Corridor
Sales | 41334 | 8241 | 1541

## Slide 7: INDUS CASCADE PAKISTAN’S MOST PRECIOUS ASSET
Indus enters Pakistan Altitude 8,430 ft
Drop of 7,840 feet
Multiple Sites along this stretch
Altitude 590 ft
42,196 MW
Skardu
Tungus
Yulbo
Bunji
Diamer Basha
Pattan
Thakot
Dasu
Tarbela/GB
Kalabagh
Shyok
640 MW
1,200 MW
2,200 MW
2,800 MW
7,100 MW
4,500 MW
4,320 MW
2,400 MW
4,673 MW
7,748 MW
3,600 MW
Jinnah
Akhori
600 MW
96 MW
Chashma
184 MW
Taunsa
135 MW
5.5 MAF
3.0 MAF
6.4 MAF
6.0 MAF
6.0 MAF
5.86 MAF
0.28 MAF
33 MAF
6
Notes: Upper Indus Basin has a drop of more than 7,000 feet in a stretch of 500 Km length which is ideal for hydropower generation and can serve as engine of growth for economy of the country. Studies carried out by WAPDA identified potential sites for hydropower development projects with more than 42,000 MW generation capacities. The important sites includes Bunji - 7,100 MW, Tungus - 2,200 MW, Yulbo - 2,800 MW, Basha - 4,500 MW, Dasu 4,320 MW, Tarbela/Ghazi Barotha - 7,748 MW, Kalabagh - 3600 MW etc.

## Slide 8
CARRY OVER CAPACITY (DAYS) – WORLD VS PAKISTAN
Days
Chart: 
| America | Egypt | Australia | South Africa | India | Pakistan
 | 900 | 700 | 600 | 500 | 170 | 30

## Slide 9
RESERVOIR | LIVE STORAGE CAPACITY |  |  | STORAGE LOSS
 | ORIGINAL |  | YEAR 2022 | YEAR 2022
TARBELA | 9.692 |  | 5.862 | 3.866 (40%)
MANGLA | 5.86 | 8.237 | 7. 356 | 0.881 (11%)
CHASHMA | 0.717 |  | 0.278 | 0.439 (61%)
TOTAL | 16.269 | 18.646 | 13.460 | 5.186 (27%)
STORAGE CAPACITY
Notes: 8
Tarbela, Mangla and Chashma are large size reservoirs in Pakistan which directly feed the Indus Basin Irrigation Network. Their original total live storage capacity was 16.27 MAF. This storage capacity was increased to 18.646 MAF in 2012 by raising of Mangla Dam.
By 2017, the total storage capacity has decreased to 13.86 MAF due to deposition of sediments. Up-till now a total storage capacity of 4.78 MAF has been lost to sedimentation, which is about 25% of original total storage capacity of these reservoirs.

## Slide 10: PROJECTS UNDER EXECUTION BY WAPDA
Mohmand Dam
(1.29 MAF, 800 MW and Water Supply 300 MGD)
Tarbela 5th Ext HP
(1530 MW)
Harpo HPP
(34.5 MW)
Diamer Basha Dam
(8.1 MAF, 4500 MW)
Nai Gaj Dam
(0.3 MAF)
Sindh Barrage
(2 MAF)
K – IV Project
(Water Supply 650 MGD)
Kachhi Canal
(30,000 Acres Land)
Kurram Tangi Dam
(18.9 MW, 16000 Acres CCA)
Dassu Hydropower
(4320 MW, 2160 MW Ph 1)
IMPACT
Gross Water Storage - 11.7 MAF
Power / Annual Energy- 9025 MW / 34.5 Billion Unit
Urban Water Supply - 950 MGD
Jobs Created - More than 35,000

## Slide 11: DIAMER BASHA DAM PROJECT

## Slide 12
Diamer Basha Dam Project is one of the most important Indus River Cascade Hydropower Project
The site Is 315 KM upstream of Tarbela Dam Project, 180 KM below Gilgit and 40 KM downstream of Chilas, the Headquarter of District Diamer GB.
It will be the tallest RCC Dam having height of 272 m and largest RCC dam in the world in terms of RCC volume (17.4 MCM).
Upon completion, it will be the 2nd largest power station in Pakistan after Tarbela having installed capacity of 4500 MW.
INTRODUCTION

## Slide 13
MAIN DAM | 
MAXIMUM HEIGHT | 272M
TYPE | ROLLER COMPACTED CONCRETE (RCC)
RESERVOIR | 
GROSS STORAGE | 8.1 MAF
LIVE STORAGE | 6.4 MAF
POWERHOUSE | 
2 | EACH LEFT & RIGHT BANK
TOTAL INSTALLED CAPACITY | 4500 MW
LOCATION | UNDERGROUND
NO OF UNITS | 12 EACH OF 375 MW
ANNUAL GENERATION | 18,100 GWH/YEAR (18.1 BILLION UNITS ANNUALLY)
SALIENT FEATURES

## Slide 14: BENEFITS OF DIAMER BASHA DAM PROJECT
INSTANT
  Jobs upto 16,500
  Engineers upto 1,050
  Steel 600,000 Tons
  Cement 2 Million Tons
  Pozzolan 2 Million Tons
  Transportation 700-800 veh/day
POST COMPLETION
  Development Rs.78 Billion
  Energy (at site) 18 billion Units
  Increase in energy at existing projects (Tarbela, GBHP, Chashma & Jinnah) 2.5 billion units
  Upcoming Projects
  (Dasu, Pattan & Thakot)
  Tarbela Life 35 Years
  Saving US$ 2.5 billion
  Agri Land 1.23 MA
7.5 billion units

## Slide 15
  DIAMER BASHA DAM PROJECT IS BEING IMPLEMENTED THROUGH THREE SEPARATE PC-Is AS FOLLOWS:
IMPLEMENTATION STRATEGY
PC-I | COST IN BILLION PKR | APPROVAL DATES | DESCRIPTION | STATUS
DAM PART | 479.686 | 14.11.2018 | CIVIL AND HYDROMECHANICAL WORKS FOR MAIN DAM AND APPURTENANT STRUCTURE | Commencement of works on 07.08.2020
ACQUISITION OF LAND & RESETTLEMENT (2ND REVISED) | 174.700 | 30.04.2020 | LAND ACQUISTION AND VARIOUS PRELIMINARY WORKS CONTRACTS, CONFIDENCE BUILDING MEASURES (CBM’S) AND CULTURAL HERITAGE MANAGEMENT PLAN (CHMP) | 91.32% Land Acquisition completed CBMs and Resettlement works in progress
POWER GENERATION FACILITIES | 933.584 | Under process | CIVIL, HYDROMECHANICAL AND ELECTROMECHANICAL WORKS FOR LEFT BANK AND RIGHT BANK POWERHOUSES | RECOMMENDED BY CDWP FOR ECNEC

## Slide 16
CONSULTANTS & CONTRACTOR
CONSULTANTS
DIAMER BASHA CONSULTANS GROUP COMPRISING OF 12 FIRMS
NESPAK (Lead Firm)
ACE - Pakistan
MMP - Pakistan
MWH (Stantec) - USA
Poyry (AFRY) - Switzerland
DOLSAR - Turkey
In association with
AGES - Pakistan
DMC - Pakistan
MAES - Pakistan
MML - UK
BIDR - China
MWH- Pakistan
Contract Cost: Rs. 27.182 Billion
Commencement: 10.06.2020
CONTRACTOR MW-1 MAIN DAM
M/s Power China-FWO (JV)
Contract Cost Rs. 442.402 Billion.
Commencement : 07.08.2020
Power China Share 70 %
FWO Share 30 %

## Slide 17
ENGAGEMENT OF PANEL OF EXPERTS
NAME | AREA OF EXPERTISE | NATIONALITY
MR. BRIAN FORBES | DAM ENGINEERING & RCC TECHNOLOGY | AUSTRALIAN
MR. CARLOS JARAMILLO | GEOLOGICAL & ROCK MECHANICS EXPERT | AMERICAN / COLOMBIAN
MR. JOHN H. GUMMER | ELECTRO-MECHANICAL EQUIPMENT EXPERT | AUSTRALIAN/ BRITISH
MR. ASLAM RASHEED | HYDRAULICS EXPERT | PAKISTANI
MR. KHALIL TAYYAB HASSAN | PROCUREMENT EXPERT | 
MR. YUSOF GHANAAT | SEISMIC DESIGN EXPERT | AMERICAN
Notes: Field Verification of existing topographic survey (carried out during feasibility study) was carried out by NESPAK Survey Team to ascertain the credibility of survey and following are the observations:
In the existing survey, NESPAK geodetic survey team observed horizontal and vertical control error in the identified control points. 63cm error in vertical control with respect to Survey of Pakistan (SOP) benchmark erected in the Primary school building in Hanzel village were observed.
Existing survey was insufficient between RD 3+300 to RD 3+700 along the Headrace Channel and along left bank of river at weir and power house site
Topographical changes were observed along the project components
Keeping in view the deficiencies in Topographic Survey, Consultants have mobilized their survey team and they carried out the acquisition of field data .Consultants Survey and GIS Experts are now processing survey data.

## Slide 18
FINANCING STRATEGY FOR PC-I: DAM PART
Project Cost
(Dam)
(Rs 480 Billion)
PSDP
(Rs 234 Billion )
Commercial Financing
(Rs 146 Billion)
Syndicate Commercial Financing
WAPDA Equity
Rs. 100 Billion
Green Euro Bond
Int’l Donor Agencies / Development Partners (SFD, IsDB, AIIB, KFD)
REVISED PC-I DAM PART IS UNDER PREPARATION. TENTATIVE COST IS RS. 707 BILLION
Notes: Field Verification of existing topographic survey (carried out during feasibility study) was carried out by NESPAK Survey Team to ascertain the credibility of survey and following are the observations:
In the existing survey, NESPAK geodetic survey team observed horizontal and vertical control error in the identified control points. 63cm error in vertical control with respect to Survey of Pakistan (SOP) benchmark erected in the Primary school building in Hanzel village were observed.
Existing survey was insufficient between RD 3+300 to RD 3+700 along the Headrace Channel and along left bank of river at weir and power house site
Topographical changes were observed along the project components
Keeping in view the deficiencies in Topographic Survey, Consultants have mobilized their survey team and they carried out the acquisition of field data .Consultants Survey and GIS Experts are now processing survey data.

## Slide 19
FINANCING STRATEGY FOR PC-I: POWER GENERATION
Project Cost
(Power Generation)
(Rs 707 Billion)
Commercial Financing
(Rs 601 Billion)
Local (Rs 200 Billion)
Banks
Sukuk Bonds
Local Bonds
Foreign (Rs 401 Billion)
Supplier’s Credit
Green Euro Bond
Panda Bond
Int’l Donor Agencies SFD, AIIB, KFD, IsDB
PSDP Funding
(Rs.70 Billion)
WAPDA Equity
(Rs. 36 Billion)
PC-I AMOUNTING TO RS. 933 BILLION (INCLUDING IDC OF RS. 226 BILLION WHICH SHALL BE RECOVERED THROUGH TARRIF)
Notes: Field Verification of existing topographic survey (carried out during feasibility study) was carried out by NESPAK Survey Team to ascertain the credibility of survey and following are the observations:
In the existing survey, NESPAK geodetic survey team observed horizontal and vertical control error in the identified control points. 63cm error in vertical control with respect to Survey of Pakistan (SOP) benchmark erected in the Primary school building in Hanzel village were observed.
Existing survey was insufficient between RD 3+300 to RD 3+700 along the Headrace Channel and along left bank of river at weir and power house site
Topographical changes were observed along the project components
Keeping in view the deficiencies in Topographic Survey, Consultants have mobilized their survey team and they carried out the acquisition of field data .Consultants Survey and GIS Experts are now processing survey data.

## Slide 20
ONGOING SITE ACTIVITIES
19
Intake Structure DT(s) & Power Waterways
Dam Right Abutment
DT(s) – Outlet Structure
Dam Left Abutment
Diversion Canal Middle & U/S Portion
Permanent Bridge – Left & Right Abutment & Piers
Foundation Pit – Block # 24
DT - 02
Guide Wall
LLO RFO Approach Area
LB Power Intake/Flushing Tunnel Intake

## Slide 21: DIVERSION TUNNEL
Inlet
Outlet
Diversion Tunnel

## Slide 22: PERMANENET ACCESS BRIDGE

## Slide 23: TEMPORARY BRIDGES
UPSTREAM
DOWNSTREAM

## Slide 24: Social Uplifting Projects
3.0 MW Hydropower Project in Thak
3.6 MW Hydropower Project in Thor
Cadet College Chilas
WAPDA Army Public School at Thor
44 No. Schemes comprising Education Development Plan, Health Sector Plan and Livelihood interventions(Water Supply, Sewerage System, Bunds etc.) of social safeguards have been completed
Composite Model Village at Harpan Das

## Slide 25
HIGH SCHOOL
POST OFFICE
SHOPPING CENTRE
MAIN MOSQUE
MODEL VILLAGE HARPAN DAS

## Slide 26
3.0 MW THAK POWERHOUSE

## Slide 27
3.6 MW THORE POWERHOUSE

## Slide 28
WAPDA CADET COLLEGE

## Slide 29
WAPDA ARMY PUBLIC SCHOOL

## Slide 30
RESETTLEMENT RELATED INFRASTRUCTURE
Right Bank Periphery Road (180.3 km)
Provision of Access to 12 No. Valleys on right bank.
RBPR-01 (27.5Km) 80.18%
RBPR-02 (51.3Km) 62.95%
RBPR-03 (51.95Km) 15.89%
RBPR-04 (24.65km) 13.20%
RBPR-00 (27Km)

## Slide 31: THANKS